## Slide 1
JD CORTEX
Perception, Reasoning, and Memory for an EZ-Robot JD Humanoid
Built on Synthiam ARC, Google Gemini, and YOLO vision
Tatheer Aima Naqvi
Vision pipeline · Gemini reasoning · Whitelisted actions · Surveillance & ambient modes
Bushra Ushaaq
Witness memory · ARC control panel · Gesture control · System launcher

## Slide 2
OVERVIEW
What JD Cortex Actually Does
Understands you
Typed, spoken, or gestured commands are understood in plain language.
Watches the room
A camera pipeline notices who is present, their posture, and what they hold.
Remembers
Arrivals, departures, and sightings are kept in a running diary.
Stays safe
Every action is checked against a fixed, pre-approved whitelist before it runs.
The core idea: sensing, remembering, deciding, and acting are handled by separate processes. Nothing is done by one giant program — which makes the whole system easier to reason about, and safer to run.
2

## Slide 3
ARCHITECTURE
Five Cooperating Processes
Vision Pipeline
camera → scene_state.json
Witness Recorder
scene state → diary
Brain (main.py)
Gemini + validation
ARC → JD
speech + movement
ARC Panel (C#)
status, diary, hold-to-talk
Gesture Control
webcam → ARC directly
Why split it up? Only main.py ever opens the ARC connection that speaks — watchers queue messages through a shared file instead of talking to ARC directly. Gesture control gets its own, completely separate ARC connection, so it can never collide with conversation.
3

## Slide 4
DATA FLOW
How One Command Reaches JD
1
Input arrives
Typed, spoken (local Parakeet), or via the ARC panel — all reach the same process_command().
2
Local match first
The text is checked against the safe-action list before anything else runs.
3
Gemini, if needed
Scene summary, witness diary, and chat history are attached to the prompt.
4
Reply is spoken
main.py sends the reply to ARC's SayWait — the only process that ever does.
5
Action re-checked
Any suggested action is validated again against known_actions.py before ARC ever sees it.
6
JD moves
A confirmed movement runs, then JD returns to Standing automatically.
4

## Slide 5
COMMAND & CONTROL
The Brain — jd_robot_system/main.py
main.py
single ARC
connection
One connection, one owner
arc_connection.py opens a single TCP socket to ARC — opened once, used for every command.
Three input paths, one brain
Console typing, local voice (Parakeet), and the ARC panel all funnel through process_command().
Validate, then act
known_actions.py holds the whitelist — movements, sounds, lights. Nothing runs without a match.
Background alert thread
Polls a file-backed speech queue so surveillance and ambient watchers can still speak safely.
5

## Slide 6
REASONING
Gemini Integration — Three Distinct Uses
understand()
Conversation & action match
Returns REPLY + MATCH. Only ever suggests an action — main.py must still validate it before it runs.
assess_alert()
Surveillance judgement
Fails SAFE: if Gemini is unreachable, it alerts anyway with a generic line rather than staying silent.
ambient_comment()
Companion remarks
Fails SILENT: if Gemini is unreachable, it simply says nothing — a skipped remark costs nothing.
Quota resilience: each call walks a list of model names — skipping to the next on a 404 — and rotates through up to three API keys per model, since the free tier allows roughly 20 requests/day/key/model. A live usage counter is shown on the ARC panel.
6

## Slide 7
PERCEPTION
Vision Pipeline — A Pure Sensor Process
Object detection
YOLO identifies general objects in frame.
Pose tracking
YOLO pose gives each person a tracker ID.
Face recognition
Matches against known_encodings.pkl to assign real names.
vision_pipeline/scene_state.json
{
"timestamp": 1723222110.4,
"objects_visible": ["laptop", "cup"],
"people": {
"3": {
"name": "aima",
"posture": "sitting",
"holding": "cup",
"sitting_on": "chair"
}
}
}
Written atomically: a temporary .tmp file is renamed into place with os.replace(...), so no reader — scene_context, the witness recorder, or the panel — ever sees a half-written file.
7

## Slide 8
MEMORY
The Witness Diary — A Robot That Remembers
SQLite
(WAL mode)
Identity by name, never tracker ID
The same person can burn through dozens of tracker IDs a minute — unrecognised sightings pool into one “unknown” bucket instead.
Debounced arrivals & departures
A couple of seconds of continuous presence confirms an arrival; a longer solid gap confirms a departure — no flapping on a tracking hiccup.
Feeds the same Gemini prompt
memory_context.py adds a diary block alongside the live scene — so “who did you see today?” is answered by the same brain as any other question.
Retention: 14 days by default (JD_DIARY_KEEP_DAYS) — pruned automatically at every recorder startup.
8

## Slide 9
INTERACTION
Hand-Gesture Control
Gesture → Action
Fist
Forward
Open hand
Stop
Index left / right
Turn
Index down
Sit
Peace sign
Wave
Three fingers
Stand
Index + pinky
Pushups
Reads a stationary webcam — never JD's own camera
JD's own camera moves when JD moves — a FORWARD gesture would shake the view, lose the hand, and trip the very safety stop meant to protect it.
Automatic safety stop
If the hand disappears mid-walk, JD is stopped automatically after a short number of hand-less frames — it can never be left walking indefinitely.
9

## Slide 10
INTERFACE
The ARC Control Panel (“Memory” Skill)
A C# ARC Behavior Control skill giving one live window into everything JD Cortex is doing.
Connection light
Live status of the link to the Python brain
Scene card
What JD currently sees, updated live
One input box
Free text for both memory questions and commands
Hold-to-talk
Push-to-record voice input from the panel
Gesture toggle
Starts/stops hand-gesture control with a plain-language legend
Guarded shutdown
A confirmed stop button for the whole system
Protocol: 127.0.0.1:5005 — one line in, one line out (status, diary [n], alerts [n], gesture on|off, listen start|stop, stop, or free text).
10

## Slide 11
SAFETY
Two Watchers, Two Failure Philosophies
Surveillance Watcher
Fails SAFE
• Watches for unknown people and sensitive objects (knives, scissors)
• A condition must persist across multiple polls before it fires
• Logs to activity_log.txt and requests a snapshot
• If Gemini is unreachable, it alerts anyway with generic wording — silence could hide a real event
Ambient Watcher
Fails SILENT
• Watches for meaningful changes — arrivals, departures, posture, idle time
• Asks Gemini whether a short remark is genuinely natural right now
• Deliberately conservative — silence is the common, expected case
• If Gemini is unreachable, it just says nothing — a skipped remark costs nothing
11

## Slide 12
UNDER THE HOOD
Tech Stack & Running the System
Vision
YOLO (ultralytics) · OpenCV · face_recognition
Reasoning
Google Gemini — plain HTTP, no SDK
Speech
Local Parakeet (sherpa-onnx) — nothing leaves the machine
Gestures
MediaPipe 0.10.21 (pinned)
Memory
SQLite, WAL mode
Control
Synthiam ARC — TCP script server, port 6666
One launcher for the whole system
python run.py check
reports every library, model file, key, and port before a session
python run.py
starts vision, memory, brain, and watchers in dependency order
python run.py --minimal
brain + witness memory only, no vision
12

## Slide 13
Thank You
JD Cortex keeps sensing, remembering, deciding, and acting as separate, cooperating processes — safe by construction, not by afterthought.
One whitelist, always checked — Gemini reasons, but never drives JD directly.
One ARC voice, one owner — every other process queues speech instead of speaking itself.
Memory by name, not tracker ID — durable, readable, and honest about what JD actually saw.
Tatheer Aima Naqvi · Bushra Ushaaq
Project: JD Cortex